## Slide 1
Lab 5 - DE1-SOC CAMERA,
VIDEO PROCESSING, AND
VGA DISPLAY
EEC 193 Digital Systems Design Project
Isidro, Justin, Max, Ricardo, Yaseen

## Slide 2
Objective
Data Acquisition: This lab focuses on interfacing the D8M-GPIO camera with the DE1-SoC to capture raw pixel data. Using the D8M_SET.v module and line buffers, we will synchronize the camera's 640×480 output with the VGA display to handle the frequency differences between the two hardware components.
Real-Time Processing: The objective is to implement hardware-level filters and interactive UI elements using Verilog. This includes performing luminance calculations for grayscale conversion via fractional multipliers, managing RGB color scaling with SW switches, and designing a responsive cursor system controlled by physical KEY buttons.

## Slide 3
Core Design Requirements
🖥
Clock Domain Synchronization
Effectively bridge the 50MHz FPGA system clock and the 25MHz VGA pixel clock. This ensures that the state machines and VGA output stage remain stable.
↔
Boundary Logic
System needs to recognize where the "walls" are, so keeping track of the cursor's position is a good technique — if you touch it, stop movement.
🎮
Interactive Controls
Like a game controller, each switch has a specified function. When you flip a switch, the system instantly updates what's on screen — color, filter, or cursor.
SW0 is reserved as the system reset signal across all filter modes.

## Slide 4
How It Works — System Architecture
D8M Camera
8MP Sensor
640×480 @60Hz
CCD_DATA[9:0]
D8M_SET.v
RAW→RGB
3× Line Buffers
R/G/B[7:0]
Video Processing Pipeline
RGB Filters
SW1-SW6
Grayscale
Lum formula
Cursor Draw
KEY0-KEY3
RGB[7:0]
VGA Display
640×480
25 MHz clk
SW Switches
SW0=Reset
SW1-SW8 filters
MIPI_BRIDGE
_Config.v
I2C Init
0x1c / 0x6c
I2C
KEY Buttons
KEY0-KEY3
Cursor move
KEY[3:0]
Clock & Reset
50 MHz PLL
25 MHz VGA
SW0=Reset
Camera
RAW Decoder
Processing
VGA Output
User Controls
I2C Config

## Slide 5
Part 1: RGB Color Filters
Overview
Each color channel — Red, Green, and Blue — can be independently attenuated using SW switches. This allows real-time selective filtering of the camera feed without stopping the pixel stream.
Intensity Steps per Channel
Each channel cycles through four levels, controlled by 2 SW switches (4 combinations):
Normal
Pass pixel value unchanged (SW = 00)
½ Intensity
Right-shift pixel by 1 bit (SW = 01)
¼ Intensity
Right-shift pixel by 2 bits (SW = 10)
Off
Output 0 for that channel (SW = 11)
Hardware Implementation
Bit-shifting is used instead of multiplication — shifting right by 1 halves the value, shifting by 2 quarters it. This is extremely efficient in FPGA fabric and requires no multiplier resources. All three channels operate in parallel on every pixel clock cycle.
SW switches are sampled synchronously — changes take effect on the next frame.

## Slide 6
Part 2: Cursor
Overview
Two cursor shapes are drawn directly onto the live video feed in blue+green pixels. The user moves the cursor with the four KEY buttons. A slow counter gates movement speed so the cursor can be positioned precisely, and boundary logic prevents it from leaving the screen.
Cursor Types
3×3 Pixel Block
A solid 3×3 square filled entirely with blue+green pixels. Simple and compact.
10×10 Pixel Box
A hollow 10×10 square with a 1-pixel border only. Interior remains transparent.
Controls & Movement
KEY0
Move Up
KEY1
Move Down
KEY2
Move Left
KEY3
Move Right
Hardware Implementation
A slow counter (variable frequency clock divider) gates cursor movement. Position registers are compared against pixel coordinates each clock cycle — matching pixels are forced to blue+green output regardless of the camera data.
Cursor color is blue+green (R=0, G=255, B=255). Boundary stops movement at col=0, col=639, row=0, row=479.

## Slide 7
Part 3: Grayscale Conversion
Overview
Color pixels from the camera are converted to grayscale in real time. The luminance value is calculated as a weighted sum of the three channels, reflecting how the human eye perceives brightness — most sensitive to green, less to red, and least to blue.
Luminance Formula
Luminance = 0.2126 x R + 0.7152 x G + 0.0722 x B
8-bit Fractional Coefficients (0.XXXXXXXX format)
Red
0.2126
x 256 = 54
8'b00110110
Green
0.7152
x 256 = 183
8'b10110111
Blue
0.0722
x 256 = 18
8'b00010010
Hardware Implementation
Three 8x8 multipliers compute the weighted products. Results are summed in an 18-bit accumulator, then bits [15:8] are taken (divide by 256). All three VGA outputs are set to the same luminance value to produce gray.
Grayscale output: VGA_R = VGA_G = VGA_B = luminance[7:0]. Coefficients sum to ~1.0 to preserve brightness.

## Slide 8
Results
RGB Color Filters
SW-controlled channel attenuation
[ Insert Screenshot ]
Cursor — 3x3 Block
Solid block cursor on live feed
[ Insert Screenshot ]
Cursor — 10x10 Box
Hollow bordered cursor on live feed
[ Insert Screenshot ]
Grayscale Conversion
Luminance-weighted output
[ Insert Screenshot ]
All filters tested on live 640x480 @60Hz camera feed — DE1-SoC FPGA platform.

## Slide 9
Conclusion
The techniques built in this lab — real-time color filtering, pixel-coordinate overlays, and luminance conversion — form the building blocks of modern video processing systems across industry and research.
01
Object Detection & Image Recognition
Grayscale conversion and color filtering are standard preprocessing steps before feeding frames into a CNN or edge-detection algorithm. FPGAs handle this entirely in hardware, reducing data bandwidth before any software model runs — enabling real-time recognition at high frame rates.
02
Medical Imaging & Thermal Cameras
Channel isolation — suppressing red or blue to enhance specific tissue contrast — is widely used in endoscopy and fluorescence imaging. The same filter architecture can apply false-color overlays or highlight anomalies on live sensor feeds with zero added latency.
03
Autonomous Vehicles & Robotics
Region-of-interest marking and pixel-coordinate tracking are the foundation of bounding-box hardware in ADAS systems. Processing these directly in FPGA fabric — rather than software — allows obstacle detection and lane marking at frame rates a CPU pipeline cannot sustain.
Key Takeaway —
FPGA hardware parallelism is what makes real-time video processing viable — the same principles used here scale directly into production systems for medical devices, autonomous vehicles, and AI vision pipelines.
EEC 181A — Digital Systems Design Project | Winter 2025 | UC Davis

## Slide 10
Problems
Justin — Getting the example project provided to work was a challenge.
The example project would not be properly uploaded onto the FPGA
The PLL was not functioning properly (was not locking correctly)
Had to use an example provided by Terasic, and change the VGA configurations to work with the monitor by looking up the correct settings

## Slide 11
💬
Questions?
Lab 5 - DE1-SOC CAMERA, VIDEO PROCESSING, AND VGA DISPLAY
FPGA Digital Design Team